## Slide 1: Workshop 3: joint design & beam balancer deliverables
Paul Groh, MME Department

## Slide 2: OVERVIEW
Joint Design:
Sleeve bearings
Roller Bearings
Examples of mounted bearings
Beam Balancer Design Problem:
Deliverables
Manufacturing locations

## Slide 3: SLEEVE BEARINGS
A Cylindrical sleeve
Sometimes referred to as a ‘bushing’
No rolling elements
Made of metal, plastic, or composite material (oil-impregnated bronze, graphite-filled PEEK, etc)
Often lubricated to reduce wear and friction
Cheap to manufacture
Suitable for low to moderate loads (~145 psi) and speed (~150 ft/min)

## Slide 4: BALL BEARINGS
Rolling-element bearing
Inner and Outer Race
Shielded or un-shielded
Made of metal, but sometimes plastic
Ideal for low to moderate loads (~145 psi) and high-speed (~500 ft/min)

## Slide 5: BEARINGS – HOW TO INSTALL INTO HOUSING
Several methods:
Method 1: Press Fit using a hydraulic or Arbor press
  Interference fit: bearing’s outer diameter is slightly larger than the bore
  Good for metal or resin printed parts
Method 2: Freeze the bearing before insertion
Method 3: Use a bonding agent
  Slip fit: Machine housing bore to recommended inside diameter for a slip fit
  Good for wood or PLA printed parts
Arbor Press
Arbor Press – Installing Sleeve Bearing

## Slide 6: BEARINGS – HOW NOT TO INSTALL

## Slide 7: EXAMPLES OF BEARINGS IN JOINTS
EXAMPLE.1
EXAMPLE.2
EXAMPLE.3
Pivot Arm Design
Mounting a shaft with 2 Ball Bearings
Revolute joint with shoulder screw
NOTE: All of these examples can be modified for sleeve bearings

## Slide 8: EXAMPLES OF BEARINGS IN JOINTS
EXAMPLE.1
Pivot Arm Design
NOTE: All of these examples can be modified for sleeve bearings

## Slide 9: EXAMPLES OF BEARINGS IN JOINTS
EXAMPLE.2
Mounting a shaft with 2 Bearings

## Slide 10: EXAMPLES OF BEARINGS IN JOINTS
EXAMPLE.3
Revolute joint with shoulder screw
NOTE: All of these examples can be modified for sleeve bearings

## Slide 11: INTRO TO BEAM BALANCER DESIGN PROBLEM
Crank mechanism with 2 linkages
Using Kinematics Model derived in class to drive the servo motor to the desired position
Space constraint
Using MG995 servo motor
3 weeks to design, build, and demonstrate
Code to run the system will be provided
  Uses a Web Cam and Arduino board to drive the Servo

## Slide 12: DELIVERABLES FOR WEEK 4 (SEPT 24)
3D Model of your design (e.g. SolidWorks)
4 minute presentation in E3-3178 during the Workshop time slots (Wed, Sept 24 9:30AM – 11:30AM)
  Show linkages and joints designs
  Describe manufacturing methods
2 minute feedback from Staff
  How to improve design
  Suggestions on how to manufacture

## Slide 13: DELIVERABLES FOR WEEK 5 (OCT 1)
Beam balancer assembled with Servo Motor
4 minute presentation in E3-3178 during the Workshop time slots (Wed, Oct 1 9:30AM – 11:30AM)
  Show progress so far
  Outline plan to demonstrate functioning system next week

## Slide 14: DELIVERABLES FOR WEEK 6 (OCT 8)
Beam Balancer Demonstration Requirements
Presentation Details:
Date & Time: Wednesday, Oct 8, 9:30AM – 11:30AM
Location: E3-3178
Format: 4-minute live demo during Workshop time slots
System Requirements:
Must balance a ball at the center of the beam.
Must return the ball to center after it is manually displaced a short distance.

## Slide 15: RESOURCES PROVIDED TO YOU
MG995 Servo with Metal Horn
  STEP File available on LEARN
M3 x 10mm SHCS, QTY 6
Web cam, Arduino, Code, Raspberry Pi 5

## Slide 16: PLACES TO GET STUFF MADE
Locations on campus to get stuff made:
WATIMAKE, DWE 3509
  WATiMake | Mechanical and Mechatronics Engineering | University of Waterloo
Engineering Machine Shop, E3
  EMS Material Store
Mention the Course and your Group # to access your team funds*
* For hardware only

## Slide 17: PLACES TO GET STUFF MADE – ORDERING FROM EMS
Visit the website to order:
  EMS Material Store
Place order AHEAD of visiting EMS!
Saves time waiting in the hall for your order to be processed!
They email you when it is ready for pick up

## Slide 18: PLACES TO GET STUFF MADE – ORDERING FROM EMS
When you are ready to order:
Press “Proceed to Order Submission”
Select “WatCard” as Material Store Payment Option

## Slide 19: PLACES TO GET STUFF MADE – ORDERING FROM EMS
3. Enter your Student Number
4. Under Team/Department, type in EXACTLY “F25MTE380G__ ”
NO reimbursement for WATCARD purchases

## Slide 20: DESIGN TIPS / MAX SPENDING LIMIT
Beam can have edges to prevent ball from falling off
Only 3D print parts that cannot be laser cut (laser cutting is faster!)
4.5 mm thick acrylic is adequate for structural parts
3 mm thick acrylic for balancing beam
Keep extra acrylic for later in the term!
Max Spending Limit, $50 per team
Size | Thickness | Cost
12” x 24” | 3.0 mm | $13
12” x 24” | 4.5 mm | $20
WATIMAKE Price List For Clear Acrylic
EMS Price List For Clear Acrylic

## Slide 21: SCHEDULE / LOCATIONS FOR WEEKS 4, 5, 6
Week 4 (Sept 24): CAD model review
Week 5 (Oct 1): Prototype review
Week 6 (Oct 8): System Demonstration
Meet each week in E3-3178 during Workshop time (9:30 AM to 11:30 AM)
  4 minutes to present

## Slide 22: WHAT TO DO WHILE WAITING FOR REVIEW
Complete Mandatory Safety Training
LEARN Course SO2500 “Risk Assessment”
Any training required for WATIMAKE (laser cutting, 3D printing)
Manufacture prototype parts (base, beam, motor mount)